## Slide 1
School of Electrical Engineering, Seoul National University
1/16
Progress of Reviewing Fast-Detrapping Retention
20240430
진명

## Slide 2
School of Electrical Engineering, Seoul National University
Content
2/16
Correction
TCAD & Model Structure
Model Comparison
Calibration Method with Constructed TCAD
    Direct tunneling
    Trap to band tunneling
Discussion about Barrier Lowering
    Proposal for the Poole-Frenkel emission under thin layer
    Evidences found in TCAD

## Slide 3
School of Electrical Engineering, Seoul National University
Correction
3/16
Nctn dependency => Vt = 1V 수준의 nctn
(Page 3 우측단 중반 중에서 [1])
Model 기준 : 에서 Vt 가 1V 증가.
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 4
School of Electrical Engineering, Seoul National University
TCAD & Model Structure for the review
4/16
Oxide envelope
(prevent LM)
CTN : fixedCharge code
Trap { (Fixedcharge conc=-4.3e18) }
Filler oxide = 17nm, Silicon = 8nm
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 5
School of Electrical Engineering, Seoul National University
TCAD & Model Structure for the review
5/16
At , BENitride cannot be fully charged by program operation
Not Trapped
Trapped
CTN Trap
=> figure 4(a) [1]
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 6
School of Electrical Engineering, Seoul National University
Model Comparison for the Review
6/16
Final Model Comparison
Temperature variation, 특정된 온도는 없음
>> 온도는 임의로 상정하여 경향성만 확인
Matched!
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 7
School of Electrical Engineering, Seoul National University
Model Comparison for the Review
7/16
TBT, DT, TE model matching
다음장부터는, DT/PF , TBT 순서로 관련 parameter 들을 이번에 설계한 oxide enveloped 구조를 통해서 calibration할 것이다.
(figure 6(a) [1] matched)
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 8
School of Electrical Engineering, Seoul National University
Direct Tunneling Calibration Method
8/16
Main Concept in TCAD Simulation
- eBarrierTunneling off
- GateCurrent(DirectTunneling) on
- PooleFenkel on
Every constants are given
Calibration :

## Slide 9
School of Electrical Engineering, Seoul National University
Direct Tunneling Calibration Method
9/16
298K
318K
338K
358K
378K
398K
Symbol = TCAD (PF, DT on) / line = model

## Slide 10
School of Electrical Engineering, Seoul National University
Trap to Band Tunneling Calibration
10/16
Main Concept in TCAD Simulation
- eBarrierTunneling on
- PooleFenkel on
Every constants are given
Calibration :
Tunneling amount average
[1] Kim, Minsoo, and Hyungcheol Shin. IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.

## Slide 11
School of Electrical Engineering, Seoul National University
Trap to Band Tunneling Calibration
11/16
Symbol = TCAD (TBT on) / line = model
2nm
298K
338K
378K
3nm
298K
338K
378K
High temperature error is due to TBT modeling assumption of making average + barrier lowering
temperature affecting TBT

## Slide 12
School of Electrical Engineering, Seoul National University
Discussion about the Result Difference
12/16
Band diagram difference over retention at TCAD / Model
Model:
Assumes conduction band in 0V at retention state
TCAD:
(-) Voltage is given at Silicon surface, inversion hole occurs at channel along retention
vs
Tunsgten
Work Function = 4.25eV
TiNitride
Work Function = 4.66eV
Difference of metal used for gate contact => Tungsten / TiNitride …
vs
=> At retention state, the difference of work function of gate metals may cause some electric field intensity difference

## Slide 13
School of Electrical Engineering, Seoul National University
Discussion about Barrier Lowering
13/16
Barrier lowering at Direct Tunneling Mechanism
If gets large enough, may occur, making emission or tunneling amount exceed capture amount.
Plus, thermal relation is observed in DT parameter calibration => this is due to Poole-Frenkel emission is dominant when TBT << DT + PF (PF < DT)

## Slide 14
School of Electrical Engineering, Seoul National University
14/16
Barrier Lowering :
Emission Length :
~ 현재 scale으로는
Barrier Lowering :
Poole-Frenkel Emission along thick layer
Poole-Frenkel Emission along thin layer
Barrier Lowering의 정도는 thin layer에서 얕아진다
Discussion about Barrier Lowering
: external Field

## Slide 15
School of Electrical Engineering, Seoul National University
15/16
time
BENitride-To2 interface faster emission
To1-BENitride interface slower emission
Evidence: Trap Charge Distribution along time
While electric field along BENitride is almost consistent
Discussion about Barrier Lowering
BENitride

## Slide 16
School of Electrical Engineering, Seoul National University
Future Works
16/16
Modify barrier lowering model for Poole-Frenkel emission
Extraction of proper barrier lowered amount along retention
relation에서 추출