## Slide 1: Modeling of Trap to Band Tunneling Detrapping Mechanism of 3D NAND Flash 진명

## Slide 2: Elastic Tunneling Current Modeling
Direct Tunneling
Trap to Band Tunneling
Elastic Tunneling Current Modeling 유도는 Appendix에서…
Result)
전체적인 modeling 식 수정 있음 (7월 자료 참고x)

## Slide 3: Capture Rate under High PV Level
[2] IEEE Transactions on Electron Devices 68.7 (2021): 3339-3345.
… not valid within Electric field!
cn motivation : Capture of free electron
Free electron capture
Electron capture in field
Electric Force
Only small portion of BETOX is involved within capture
(if )
Effective capture portion
(no capture)
Effective capture coefficient fc < 1

## Slide 4: Fitting Parameter & TCAD Calibration
Fitting Parameter : Vch >> Differs by PV level, set by TCAD result
1us program
~ 1.7 V
~ 0.9 V
0.2us program
WLT = 0V
>> Vch 를 TCAD로 구한 이후 해당 PV level에서 parameter 반영
Hole inversion due to CTN charge
hDensity high
hDensity high

## Slide 5: Model Observation
Currently applied fitting parameter :
Direct Tunneling x-sectional area coefficient, aDT = 1
Trap to Band Tunneling x-sectional area coefficient, bTBT = 0.3
Effective Capture coefficient, fc = 0.01
Et = 0.8 eV
TBT on / PF and DT off
Temperature independent
TBT off / PF, DT on
Temperature Dependency
Model
TCAD

## Slide 6: Model Observation
Comparison of Model & TCAD
TBT, PF, DT on - TCAD
TBT, PF, DT on - Model
TBT dominant
DT dominant
경향성 비슷한 상황 >> Calibration 진행 가능
TBT dominant
DT dominant

## Slide 7: Trap Distribution Simulation
6월 연구미팅 자료
Trap Distribution Simulation
>> 그대로 적용
TBT dominant
DT dominant
TBT dominant
DT dominant
Et = 0.85 eV, sig = 0.25 eV, Gaussian

## Slide 8: Future Works
Detail calibration of Parameters : aDT , bTBT , fc
Fitting parameter 특징 분석 & 물리적 타당성
Distribution Simulation Completion

## Slide 9: Appendix Elastic Tunneling 정리 진명

## Slide 10: Tunneling Coefficient
The WKB Approximation
…

## Slide 11: Elastic Tunneling of Electron
Main Assumption
Energy level of electron conserves in tunneling procedure
Fermi level depends on the operation of the device
At FN tunneling state, Fermi level is above the conduction band level
At retention state, Fermi level is about trap level
FN tunneling state in high current
Direct tunneling state in Retention
Electron gas in Conduction band
~ Boltzmann Distribution
Excessive electron current
~ Step function
Trapped electrons

## Slide 12: Tunneling Current Modeling
Conventional Current Density:
By quantum relation,
Occupied electron state : f1(ε)
Available electron state : 1 - f2(ε)
TC
Area

## Slide 13: Direct Tunneling
: Duke’s Tunneling Current Model
Quasi-Fermi level
DoS of periodic space

## Slide 14: Direct Tunneling
a: Area correction parameter (default = 1)
TC(EC)

## Slide 15: Localization of Trapped Electron
Trapped electron is localized within the trap nitride device structure.
: Trapped electron modeled as Aperiodic cubit trap site
(cf. cubit in size of atom, finite potential well)
~0.1Å
Wilhelmer, Christoph, et al. Nanomaterials 13.16 (2023): 2286.

## Slide 16: Trap to Band Tunneling
: Trap-to-Band Tunneling Current Model
Activated energy of the trap device : the energy activated by barrier lowering!
, (Et : ground state of the trapped electron)
>> is lowered barrier by Poole-Frenkel emission
Assumption:
Trap = Aperiodic potential well
DoS of aperiodic cubit

## Slide 17: Trap to Band Tunneling
: Trap-to-Band Tunneling Current Model
Trap to Band Tunneling
Effective Area :
~0.1Å
TC
: electron matter wavelength
b : volume correction parameter
(ground state of trapped electron)
(maximum state of trapped electron)
: Lowered Barrier (by Poole-Frenkel)

## Slide 18: Trap to Band Tunneling

## Slide 19: Trap to Band Tunneling

## Slide 20: Trap to Band Tunneling
Idea of the modeling
Proposed TBT
Conventional TBT
각각의 전자들이 별개로 움직임
Trap 된 전자들은 모두 동일한 tunneling current
TC
TC
TC
TC
TC
Tunneling current

## Slide 21: Final Result
Direct Tunneling
Trap to Band Tunneling