## Slide 1: Modeling of Detrapping electron in BE-TOX by Elastic Tunneling Emission 20241129 진명

## Slide 2: NonLocal Tunneling in TCAD
ox1 layer
n1 layer
ox2 layer
CTN
BE-TOX (ONO)
Interface – trap coupling
Coupled trap – interface 관계가 SRH theory와 같은 steady state 상태에서 이루어짐
+
Nonlocal tunneling = Elastic + phonon-assisted
WL
WL
WL
Channel
CTN
Nonlocal mesh
: interface – mesh(trap) coupling

## Slide 3: Elastic Tunneling Capture & Emission
ox1 layer
n1 layer
ox2 layer
CTN
BE-TOX (ONO)
Since Etrap>> EFi , emission >> capture
Trap – to – Band emission occurs

## Slide 4: Channel Potential
CTN programmed electron forms negative voltage
>> hole accumulation at channel
Vch
Negative channel potential bias!
20V single pulse 1us program:
Vch = -1.9V
(Can be specified for certain PV level)

## Slide 5: TCAD & Modeling Method
WL
Channel
BE-TOX
CTN
Box
TCAD Setting
BETOX oxide envelope
> No lateral spreading occurs
CTN CCS Nullification (~ 0)
> Ideal electron retention
BE-TOX
Modeling Setting
Modeling designed with vertical segments

## Slide 6: Modeling Method of Coordinate Segment
ox1 layer
n1 layer
ox2 layer
CTN
BE-TOX (ONO)
BE-TOX
“Centered balance point”
λ used as a fitting parameter
(0< λ<1)
λ
1-λ
Fn, j
Fox
(rtox,center)
coordinate
Energy Band

## Slide 7: Transmission Coefficient
jth segment along total Vsol segments
①
②
①
②

## Slide 8: Result of Elastic Tunneling Model
Result and comparison with TCAD simulation
0.6 eV Elastic
0.8 eV Elastic
1.5 eV Elastic
Sharing parameter : λ = 0.9
: total 7 segments
Location
correction
λ = 0
λ = 1
Vsol = 7

## Slide 9: Phonon-assisted Model
1.5 eV Elastic
Detrap이 끝나갈 쯤, TCAD에서는 detrap 가속화
>> Phonon-assisted

## Slide 10: Phonon-assisted Model Result
1.5 eV Elastic
1.5 eV Phonon-assisted
0.6 eV Phonon-assisted
0.8 eV Phonon-assisted
Wph = 0.06 eV
Wt = Et
Wopt fitting result in 2nd order
Wopt = Et + (Et+0.2)2
Detrapping over time
앞부분 부터 elastic으로 빠짐
남아있는 뒷부분은 Phonon-assisted
Because…
elastic
Phonon-assisted
Elastic 과 거의 차이 없음

## Slide 11: Summary
: Trap-to-Band elastic tunneling emission rate
Elastic Tunneling TCAD Fitting
Phonon-assisted correction in deep trap

## Slide 12: Appendix Elastic Tunneling Interface-Trap coupling

## Slide 13: Interface-Trap Coupling by Elastic Tunneling
Principle of Detailed Balance
Similar to SRH recombination-generation theory,
Emission of electron/hole is in steady state coupled to tunneling from carrier reservoir
(in this case, carrier reservoir is CB of channel)
ox1 layer
n1 layer
ox2 layer
CTN
BE-TOX (ONO)

## Slide 14: Capture Rate by Elastic Transition
: Transition rate by Fermi golden rule
: Constant perturbation of energy band by trap
: Unperturbed energy band free electron
: Trapped electron
Constant Trap
Free wave eq.

## Slide 15: Capture/Emission of Nonlocal Tunneling