## Slide 1: 26년 5월 연구미팅 자료 진명

## Slide 2: Time-step-free Model Impact
ΔVth : Equivalent channel field intensity
By Cramer’s rule,
ΔVth Calculation Optimization

## Slide 3: Time-step-free Model Impact
Property
Transient TCAD
Time-step-free model
Temporal
treatment
Sequential
time stepping
Final-time
dependence
Runtime grows as
simulated retention time increases
Independent of final
physical time for fixed queries
Average
runtime
27483 s
3.926 s
Closed-form evaluation
≈ 7000×
runtime reduction
TCAD 는 final physical time까지 time step 별 순차적으로 계산
Time-step-free model은 closed-form evaluation
Computational resource는 final retention time 자체가 아니라 trap bin 수와 evaluated time point 수에 의해 결정

## Slide 4: Time-step-free Physics-based Modeling
Main Idea: simulation done with initial condition
=> different from time stepping transient simulation
1. Initial state
nt0(r, Et)
2. Emission rates
ech, eWL
3. Direct evaluation
nt(r, Et, t)
계산 비용은 final retention time 자체가 아니라
trap bin 수와 evaluated time point 수에 의해 결정

## Slide 5: Time-step-free Physics-based Modeling
Main Idea: simulation done with initial condition
=> different from time stepping transient simulation
1. Initial state
nt0(r, Et)
2. Emission rates
ech, eWL
3. Direct evaluation
nt(r, Et, t)

## Slide 6: Time-step-free Physics-based Modeling
computation resource는 final retention time 자체가 아니라
trap bin 수와 evaluated time point 수에 의해 결정
Main Idea: simulation done with initial condition
=> different from time stepping transient simulation
1. Initial state
nt0(r, Et)
2. Emission rates
ech, eWL
3. Direct evaluation
nt(r, Et, t)
Initial state
closed-form evaluation
Detrapping Autonomous ODE
: Autonomous ODE

## Slide 7: ΔVth Simulation over Variations
Shallow trap retention variation dominant
Deep trap retention distribution widening starts
Deep trap retention variation dominant
ΔVth Simulation over TOX variations
Trap Profile
Initial Vth
Shallow Trap:
narrow distribution, fast
Deep Trap:
wide distribution, slow
Initial Vth

## Slide 8: Future Works
Extension to more parameter variations >> TOX 이외의 CTN, BOX 두께, trap profile 등의 여러 변수들에 대해서도 산포 변화 분석
Time dependent sensitivity analysis of retention loss >> shallow/deep trap에서의 시간에 따른 dominancy가 어떻게 변하는지
Statistical Modeling of Vth distribution evolution >> 각각의 변수들이 산포의 표준편차에 반영되는 정도를 모델링